## Slide 1: AI-Integrated GPS-Denied Autonomous Drone
PROJECT REVIEW · [DEPARTMENT, INSTITUTION]
Vision-based navigation hand-over for a small multirotor, built on ROS 2 and a Raspberry Pi 5
Team
[Member names and roll numbers]
Guide
[Guide name]
Date
October 2026
Notes: Introduce the team and the guide. One sentence on the project: a drone that keeps navigating when GPS is lost, using a stereo camera, and reports what objects it sees.

## Slide 2: Problem Statement
01
Small drones rely on GPS to hold position. When the signal is blocked or unreliable, they drift until a pilot takes over.
The project builds a drone that notices GPS degrading and keeps holding position and flying short routes using its own cameras and inertial sensors.
Where GPS fails
Indoors and under roofs
Under tree canopy
Between tall buildings
Near radio interference
Project title
AI-Integrated GPS-Denied Autonomous Drone
GPS-Denied Autonomous Drone
2
Notes: A typical college or hobby drone falls back to altitude-hold when GPS is lost and drifts with the wind. We want it to continue safely on vision. GPS loss is always simulated in our tests; we never jam GPS.

## Slide 3: Abstract & Introduction
02
A Raspberry Pi 5 running ROS 2 reads a stereo camera and an inertial sensor, estimates the drone's motion by visual-inertial odometry, and computes depth. A flight controller running ArduPilot fuses that estimate with its own sensors.
While GPS is healthy the vision estimate is aligned to it in the background. When GPS is judged unusable, the flight controller is told to switch its position source to vision. A small neural network labels objects in view and stereo depth gives their distance.
A safety pilot can take control at any time.
Objectives
1
Detect GPS degradation before position is lost
2
Hand over to vision without landing
3
Sense obstacles ahead and stop
4
Report objects with class and distance
GPS-Denied Autonomous Drone
3
Notes: Stress that the flight controller always flies the vehicle. The Raspberry Pi only supplies measurements and slow setpoints. The neural network adds object labels; it is not what keeps the drone localised.

## Slide 4: Literature Survey
03
Work | Approach | Relevance to this project
OpenVINS, Geneva et al., 2020 | Filter-based stereo VIO (MSCKF) | Light enough for a Pi 5; estimates camera–IMU time offset online
VINS-Fusion, Qin et al., 2019 | Optimisation-based stereo VIO | Accurate but heavier; ROS 2 only through community ports
ORB-SLAM3, Campos et al., 2021 | Visual-inertial SLAM with loop closure | Too heavy for a shared CPU; no official ROS 2 support
RTAB-Map, Labbé & Michaud, 2019 | Graph SLAM with stereo odometry | Usable as a visual-only backup odometry
Delmerico & Scaramuzza, 2018 | Benchmark of VIO on embedded boards | Filter-based methods suit small processors
Gap: published results assume global-shutter, hardware-synchronised cameras. Little is reported for low-cost, unsynchronised stereo modules.
GPS-Denied Autonomous Drone
4
Notes: We also relied on ArduPilot's own documentation for GPS / non-GPS transitions using EKF3 source sets. Our camera has no hardware synchronisation and uses rolling-shutter sensors, so measuring how well VIO works on it is part of our contribution. Verify the exact citation details before the final report.

## Slide 5: System Architecture
04
Stereo camera + IMU
Two image sensors, 60 mm apart
Raspberry Pi 5 · ROS 2 Jazzy
Visual-inertial odometry
Stereo depth
Localisation manager
Object detector
Navigation-mode manager
Navigator and safety
MAVLink over UART
Pixhawk 6C · ArduPilot
Sensor fusion (EKF3), flight control, failsafes
ESCs and motors
Directly into the flight controller: GPS and compass, optical flow and range sensor, RC from the SIYI MK15.
Design rule: the flight controller flies; the Raspberry Pi advises. The drone stays flyable with the Pi unplugged.
GPS-Denied Autonomous Drone
5
Notes: The Pi sends three things to the flight controller: a vision pose estimate, obstacle distances and slow position or velocity setpoints. The flight controller sends back its state, GPS quality and EKF status. RC goes straight to the flight controller, so the pilot's override never passes through the Pi.

## Slide 6: Software Requirement Specification
05
Functional requirements
Fly on GPS when GPS is healthy
Monitor GPS health and declare denial within 3 s
Switch position source to vision without landing
Produce a depth image and stop for obstacles ahead
Detect objects and report their distance
Log every mode change and every flight
Allow manual override at any time
Non-functional targets
Measure | Target
Odometry update rate | ≥ 20 Hz
Left/right camera skew | ≤ 1 ms
Odometry drift | ≤ 2 % of distance
Position hold on vision | ≤ 0.5 m RMS
Object detection rate | ≥ 5 Hz
CPU load on the Pi | ≤ 75 %
Design targets. Nothing has been measured yet.
GPS-Denied Autonomous Drone
6
Notes: The full specification lists every functional and non-functional requirement with an ID and a verification method. These are the headline ones. Be clear that the numbers on the right are targets we will test against, not results.

## Slide 7: Proposed System
06
Four navigation tiers. Each one needs fewer sensors than the tier above it, so every failure has somewhere to fall.
Tier 1
GPS
Normal outdoor flight. Vision runs in the background and is aligned to GPS.
Tier 2
Vision
GPS denied. Stereo visual-inertial odometry feeds the flight controller.
Tier 3
Optical flow
Vision lost. A downward sensor holds position without the Pi.
Tier 4
Hold height, land
No position source. Pilot takes over, or the drone lands.
What the project adds: a hand-over manager that scores how far vision can be trusted, and switches the flight controller's position source only when that score is high.
GPS-Denied Autonomous Drone
7
Notes: The tiers map one-to-one onto ArduPilot's three EKF source sets. The pilot can also force a tier with a switch on the remote. Tier 2 is the focus of the project. Tier 3 exists so that a crash of the Raspberry Pi does not leave the drone drifting.

## Slide 8: Module Split-up
07
1. Sensing
Synchronised stereo capture and inertial data with accurate timestamps
2. Stereo depth
Rectification, disparity, depth image, obstacle distances by sector
3. Odometry
Visual-inertial pose and velocity, with a health monitor
4. Localisation
Aligns vision to the autopilot frame and scores confidence
5. Mode manager
Classifies GPS health and selects the navigation tier
6. AI perception
Object detection, then range and position from depth
7. Navigation
Waypoint following, speed limits, stop for obstacles, missions
8. Safety
Watchdogs, pre-flight check, telemetry to the ground station
Implemented as 19 ROS 2 packages. Modules talk only through defined topics, so the camera or the odometry can be replaced without touching the rest.
GPS-Denied Autonomous Drone
8
Notes: Suggested split of work: one member on sensing and stereo depth, one on odometry and localisation, one on the mode manager, navigation and simulation, one on AI perception and the vehicle build. Adjust to the team.

## Slide 9: Algorithms & Techniques
08
Technique | Used for
Multi-state constraint Kalman filter | Visual-inertial odometry from stereo images and IMU
Extended Kalman filter (ArduPilot EKF3) | Vehicle state; switching between GPS, vision and flow
Stereo block matching | Disparity and metric depth, Z = f·B / d
4-DoF frame alignment | Relating the drifting vision frame to the autopilot frame
State machine with hysteresis | GPS health classification and tier selection
YOLO26n convolutional detector | Object detection at 320 px on the Pi's CPU
Late fusion of boxes and depth | Object range and position on the map
Geometry does the localising and the obstacle sensing. The neural network only answers “what is it?”.
GPS-Denied Autonomous Drone
9
Notes: The odometry is OpenVINS. A visual-only stereo odometry (RTAB-Map) is the backup, and a small OpenCV stereo odometry is our own simplified version for learning and validation. Confidence is the minimum of several independent checks, including comparison with the flight controller's own gyro and barometer.

## Slide 10: Software Tools & Technologies
09
Platform
Ubuntu 24.04
ROS 2 Jazzy
C++17
Python 3.12
Flight stack
ArduPilot Copter 4.7
MAVLink 2
MAVROS
QGroundControl
Vision and AI
OpenCV
OpenVINS
NCNN runtime
YOLO26n
Kalibr
Simulation and test
ArduPilot SITL
Gazebo Harmonic
RViz2
rosbag2
pytest, GoogleTest
Hardware: Raspberry Pi 5 (8 GB) · Waveshare IMX219-83 stereo camera · Holybro Pixhawk 6C · SIYI MK15 · MTF-01 optical flow sensor
GPS-Denied Autonomous Drone
10
Notes: All software is open source. We rejected ORB-SLAM3, Nav2, MAVSDK and running PyTorch on the drone, each for a recorded reason. The Pi, camera and MK15 are already owned; the Pixhawk and flow sensor are to be bought.

## Slide 11: Project Plan 2.0
10
Stage | Work | Exit gate
1. Design | Requirements, architecture, decisions | Design accepted
2. Simulation | Autopilot in the loop, mode manager | Works in simulation
3. Sensors and perception | Camera, calibration, odometry, detector | Camera suitable
4. Vehicle integration | Flight controller, wiring, bench tests | Safe to fly
5. Flight testing | Shadow mode, hand-over, waypoints | Hand-over reliable
Simulation first
Software progresses while hardware is on order
Early camera decision
Keep or replace the camera on measured results
Three delivery levels
Simulation, then hover hand-over, then waypoints
GPS-Denied Autonomous Drone
11
Notes: Stages 2 and 3 run in parallel. No autonomous flight happens until simulation, hardware-in-the-loop and bench tests have passed. If hardware or weather delays us, the complete simulation plus bench results is still a finished project.

## Slide 12: Project Scope, Feasibility & Requirements
11
In scope
Position hold on GPS and on vision
Automatic hand-over between them
Short waypoint routes up to 2 m/s
Stopping for obstacles ahead
Object detection with distance
Out of scope
Night or featureless scenes
High-speed or long-range flight
Planning a path around obstacles
Map building during flight
Any real GPS jamming
Feasibility
Technical: open-source stack; the autopilot already supports vision input.
Economic: computer, camera and radio are owned. About ₹54,000 to ₹1,12,000 more, estimated.
Operational: under 2 kg, line of sight, safety pilot always present.
GPS-Denied Autonomous Drone
12
Notes: The cost range is wide because the airframe is not yet chosen and component prices vary between sellers. If the institute can lend a 450 to 500 mm quadcopter, batteries and a charger, the extra spend roughly halves. GPS loss is simulated with an autopilot switch.

## Slide 13: Timeline & Milestones
12
Week
1
10
20
30
Design and set-up
Simulation and navigation logic
Sensors, odometry, AI
Vehicle build and integration
Flight testing
Evaluation and report
Week 3
Design accepted
Week 13
Camera decision
Week 20
Simulation demo
Week 22
Cleared to fly
Week 27
Hand-over in flight
Week 34
Final demonstration
GPS-Denied Autonomous Drone
13
Notes: About 34 weeks, two semesters, for a team of three or four working part-time. These are planning estimates. If only one semester is available, the realistic end point is the week 20 simulation demonstration plus bench results from the real camera.

## Slide 14: Risk Identification
13
Risk | Likelihood | Impact | Mitigation
Camera unsuitable for odometry: rolling shutter, no hardware sync | High | High | Measured go/no-go at week 13; backup estimator; upgrade path named
Pi 5 CPU cannot run odometry, depth and AI together | Medium | Medium | CPU budget per module; AI and video shed first
Position jump when switching source | Medium | High | Continuous alignment beforehand; first switches in a tethered hover
Crash during testing | Medium | High | Eight test levels before autonomy; safety pilot; spare parts
Schedule overrun | High | Medium | Simulation first; three delivery levels
GPS-Denied Autonomous Drone
14
Notes: The camera is the main technical risk. Its vendor states it has no hardware synchronisation. We keep it because it is already owned and because measuring how far it can go is itself a useful result. A fuller failure analysis with 47 items is in the project documentation.

## Slide 15: Thank you
CURRENT STATUS
Design baseline complete. Next: procure the flight controller and set up the simulation.
Decisions needed from the review
Airframe · objects to detect · one or two semesters
Notes: Close by asking for the three decisions: which airframe we may use or buy, which object classes the demonstration should detect, and whether the project runs for one or two semesters. Then take questions.